## Slide 1: iCMR January 28, 2016
Meir Dahan
Executive Vice President R&D / CTO
by Deerfield Imaging, Inc.

## Slide 2: Combined MRI and X-ray Angiography System
Artis Zee
Espree / Verio

## Slide 3: Technical and Clinical Challenges
  Preserve all existing Angio system functionality and performance
  Angio system needs to be RF quiet during MR imaging
  Angio components near the magnet must be MR conditional or safe
  For cardiac MR imaging, need a mechanism to install posterior RF coil and removal for X-ray imaging without affecting the patient
  Emergency bailout imaging; rapid transition from MR imaging to intervention without patient transport
  MR safe Hemodynamic monitoring and recording devices

## Slide 4: Typical System Layout

## Slide 5: Cardiovascular Configuration
  Designed MR and X-ray compatible components
  Designed a cardiac coil “cavity” to allow insertion and removal of the cardiac coil for MR imaging
  Designed MR conditional patient table

## Slide 6: Angio Power Up/Down
When the magnet moves past the Patient Safety Check Point (PSCP), all components in the Angio room automatically power down/up (including the Angio system)
Magnet
PSCP

## Slide 7: Treating patients with Atrial Fibrillation Recurrence After Prior AF Ablation (N=10)
MRI data transferred to EAM station. X-ray, ULS & EAM -guided intervention performed.
Prepare Room, Bring MRI back in
Perform MRI Imaging
to find gaps in ablation lesions
Remove MRI. Prepare OR
for EP Intervention
OR Room (EAM, ULS, X-ray)
MRI Room
Perform MRI. Validate Lesion Gap Closure
IMRIS solution to patient handling No patient motion between OR and MRI

## Slide 8: Acute MRI Contributions after EP ablation Lumen Imaging, Scar Imaging, Edema Imaging
RIPV
LIPV
RSPV
LSPV
LA
Schmidt/ BWH

## Slide 9
LSPV
LIPV
RIPV
LSPV
RIPV
LIPV
LSPV
RSPV
LIPV
RSPV
Late Gad Enhancement
Pre-ablation
Detect Scar Gaps
Late Gad Enhancement post-ablation
Confirm gap closure
EAM Mapping (St. Jude) Pre-ablation
Confirms Ablation Lesion Gaps
Schmidt/ BWH
Grey: Scar Circles : gaps detected with MRI
Ablate Gaps
No recurrences (N=10) 3+ yrs. post-ablation
IMRIS MRI
Room
IMRIS OR Room
Human MR-Guided Left Atrial Radio-Frequency
Repair Ablations

## Slide 10: Future Technology Development
Artis Q Zen
New X-ray Tube
(GIGALIX X-ray tube)
New X-ray flat panel detector (HDR detector)
Same X-ray Tube
as Artis Q
New X-ray flat panel detector for low dose
(Crystalline silicon detector)
Artis Q
Aera/Skyra