## Slide 1: Real-Time Image-Based Motion Compensation
Graham Wright
Sunnybrook Health Sciences Centre, University of Toronto
SCMR Interventional Workshop
Jan. 28, 2016
University of Toronto

## Slide 2: Disclosures
I have the following conflicts of interest to disclose with regard to the subject matter of this presentation:
GE Healthcare – Research Support
HeartVista – Research Support
Graham Wright, PhD

## Slide 3: Image Registration for Motion Compensation
Context:
  Current clinical tools merging prior CT/MR roadmaps with electroanatomic maps via landmarks and overlay on x-ray to guide ablation procedures yield positional error as much as 2.1±1.1 cm, primarily due to motion1
  Model-based motion compensation misses intra-procedural variability
  Realtime imaging offers limited depiction of target anatomy (poor contrast, 2D)2
  Motion correction with realtime imaging can yield most accurate target position
H. Zhong et al. Heart Rhythm, 2007
A.C. Lardo et al. Pediatr Cardiol, 2000

## Slide 4: Direct Motion Correction in Heart using Realtime MRI
Registering 3D prior volume to 2D RT image should improve the anatomical localization of the interventional catheter.
Approach: Use an edge-sensitive multi-scale registration algorithm to achieve the desired accuracy
Realtime 2D MRI
Catheter Position
+
Register
Prior Volume
Notes: …leading to improved RF ablation targeting accuracy.

## Slide 5: Edge-Preserving Denoising with Weighted Total Variation
t
prior
real-time
P. Athavale et al. Medical Image Analysis 2015
Notes: -de-noising and edge preserving algorithm…

## Slide 6: Edge Sensitive Registration
Evaluated a number of registration metrics. The best results were achieved by using an edge sensitive metric - normalized gradient fields (NGF)1
1. E. Haber and J. Modersitzki MICCAI 2006
prior
RT
align

## Slide 7: Registration Framework and Results
(a)
(b)
(c)
R. Xu et al. IEEE TBME 2014
Normalized Gradient Fields
Normalized Cross Correlation
Mutual Information
Notes: multiscale registration motivation
robustness
speed

## Slide 8: Realtime Motion Correction
R-R interval: 1000 ms
200 ms
diastolic window
Ideally image registration should be complete in < 200 ms; this is challenging (MATLAB implementation is ~30s).
Alternatively, a rapidly updated (<1000ms) motion model can be used to predict motion.
Heart Rate: 60 BPM
Notes: -actually < 200 ms due to time required for data acquisition/reconstruction -> RT image

## Slide 9: GPU Based Image Registration
This GPU registration framework reduces image registration time from ~30s to ~200ms.
Operation | Time
CPU-to-GPU Memory Transfer | 1.45 ms
Weighted TV processing / slice | 25 ms
Multiscale optimization loop | 176 ms
Total | 202.45 ms
Notes: NGF distance transfer takes approximately 0.01 ms (measurement resolution ~0.05us)

## Slide 10: Realtime Registration for Dynamic Motion Modeling
R. Xu et al. IEEE TBME 2015

## Slide 11: Respiratory Motion Model
R. Xu et al. IEEE TBME 2015

## Slide 12: Dynamically Updated Motion Model
Predict Motion
Estimate
Build Motion Model
Notes: -Model building itself requires ~8 ms
-fast because linear least squares fitting has a closed-form solution.
- x = inv(ATA) ATb (solution to Ax = b) or min x ||b-AX||2

## Slide 13: Dynamically Updated Motion Model
Predict Motion
Estimate
Build Motion Model

## Slide 14: Dynamically Updated Motion Model
Predict Motion
Estimate
Build Motion Model

## Slide 15: Evaluation
Before
Motion Model
Correction
After
Motion Model
Correction
prior
real-time
A
B
A
B
APD
DSC = 2 (A & B) / (A + B)
Notes: DSC = 2 (A & B) / (A + B)

## Slide 16: Results
Overall motion correction results from all 8 volunteers studies. Mean ± SD for (a) DSC and (b) APD after image registration (1 heart cycle delay), static model correction, and dynamic correction respectively.

## Slide 17: Results
breathing
variations
begin
Representative volunteer case study, comparing the 3 different motion correction approaches.

## Slide 18: Summary
Realtime image registration for motion compensation holds potential for more accurate intervention guidance
GPU accelerated multi-scale edge-based LV registration of realtime MR and prior 3D MR volumes achievable within 200ms
This registration, with adaptive motion model, yields robust motion correction in volunteers

## Slide 19: Acknowledgements
Robert Xu
Prashant Athavale
Kevan Anderson
Bonny Biswas
Venkat Ramanan
Rhonda Walcarius
Kawal Rhode, KCL
Canadian Institutes of Health Research
Federal Development Agency of Canada
Ontario Research Fund