## Slide 1: Interventional CMR Course Real-time Phase Contrast MRI: Present & Future
Rajiv Ramasawmy, PhD
Laboratory of Cardiac Intervention
National Heart, Lung and Blood Institute
Thursday 1st February 2018
CMR 2018

## Slide 2
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Disclosures
I have no financial interests or relationships to disclose with regard to the subject matter of this presentation.

## Slide 3
Fick
Estimated VO2
Blood sampling
Thermodilution
Regurgitation/shunt insensitive
Limited repeats
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Measuring cardiac output
Ultrasound
- Real-time stroke volume (mL)
Cardiac output (L/min)
Haddad 2009
iCMR: Beat-to-beat CO to guide provocations
Pulmonary vascular resistance (PVR)
Notes: WHY do we want beat-to-beat?

## Slide 4
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Phase Contrast MRI 101: Velocity Encoding
Gradients (G)
Phase (φ)
static
moving
Slice exc.
Imagacq.
= 0
≠ 0
Phase world
static
moving
Space
Magnetic field
time
time
“flow compensated”
“flow encoded”
“phase difference”
Real world

## Slide 5
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Phase Contrast MRI 101
Dyverfeldt 2015
4D flow
2D flow
Robust
Stroke volume
Cardiac output
Free-breathing, retrospectively ECG-gated acquisition at high spatial resolution ~2-3 minutes
Pretty pictures
Visualize abnormal flow
Wall shear stress
CFD of intervention outcomes
Free-breathing, retrospectively ECG-gated acquisition ~ 15-20 minutes

## Slide 6
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Real-time flow
Temporal resolution: 40 ms/25 fps
Spatial resolution: 2.5 x 2.5 mm2
(4D flow CMR consensus statement, Dyverfeldt et al., 2015)
Exercise/pediatric heart rates ~140 bpm (~ 15 ms/65 fps temp res)
Rogers 2017
Non-acc Acq. | Temp res. | Frames/sec
Cartesian | 200 ms | 2.5
EPI | 100 ms | 10
Radial | 350 ms | 2.9
Spiral | 100 ms | 10
Flow
Time
Catheter-guiding real-time ~10 frames/sec

## Slide 7
Spiral
EPI
Radial
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Real-time flow – MRI acquisition methods
Cartesian
Spiral
Radial
Accelerated
7
“Swirl”
“Wrap”
“Streak”

## Slide 8
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Image reconstruction
FT
IFT
GRIDDING
GRAPPA
Iterative SENSE
t
k
Temporal encoding
Sparse encoding

## Slide 9
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Ideal real-time workflow
1
2
3
4
5
1
2
3
4
1
2
3
4
Acquisition (temporal resolution)
Reconstruction
Processing
Feedback

## Slide 10
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
“Real-time” image reconstruction
Temp. res | Recon. latency | Technique (source)
44 ms | 27 ms | Spiral flow SENSE (Kowalik 2012)
50 ms | 48 ms | radial SENSE (Sorenson 2009)
40 ms | 160 ms | Radial flow (Joseph 2014)
18 ms | 116 ms | Spiral GRAPPA (Lingala 2017)

## Slide 11
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Image Analysis
Segmentation
Manual: 12 s/frame
Automatic: 70 ms/frame
Real-time data can self-generate bins for registration
Motion correction
Gadgetron: Open-source and in-line
Real-time with MoCo
Barber 2016
Odille 2011

## Slide 12
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Real-time flow examples: Past and present
Sun 2017
Barber 2016
Gatehouse 1994
Joseph 2012
Nezafat 2005
Markl 2015
Koperich 2012
Jones 2011

## Slide 13
Interventional CMR | Real-time Phase Contrast MRI: Present & Future
Future methods and applications
Methods:
Machine-learning to accelerate reconstruction and analysis
Cloud reconstruction
Tan 2018
Miller 2016
Sinning 2013
iCMR real-time flow applications:
Pressure-Volume loops
Trans-catheter valve replacement assessment

## Slide 14
  Robert J. Lederman, MD
  Kanishka Ratnayaka, MD
  Elena Grant, BM BCh
  Toby Rogers, BM BCh
  Jaffar Khan, BM BCh
  Dan Herzka, PhD
  Anthony Z. Faranesh, PhD
  Michael S. Hansen, PhD
  Adrienne Campbell-Washburn, PhD
  Peter Kellman, PhD
  Hui Xue, PhD
  Matthew Restivo, PhD
  Mahamadou Diakite, PhD
  Burcu Basar, BSc
  Delaney McGuirt, BS, RT
  Jonathan Mazal, MS, RA
  William H. Schenke, BS
  Katherine Lucas
  Laurie P. Grant, RN, NP
  Annette M. Stine, RN
  Jennifer Steeden, PhD - UCL
  Acknowledgements:
rajiv.ramasawmy@nih.gov