## Slide 1: MRI catheterization guide wires
Christian Meierhofer
Pediatric Cardiology and Congenital Heart Disease
German Heart Center Munich
Technical University of Munich
Germany

## Slide 2
PA, VSD
till age of 12 yrs - 17 cathlab procedures

## Slide 3: Guide wires…
Made of stainless steel or metallic alloys
- guides - the catheter through blood vessels and heart structures
often PTFE coated soft tip
  Less trauma to intima wall
Flexible tip and rigid end
Solid guide wires
    Less cath tip flaring, vessel damage, blood clotting
Wrapped guide wires
  More versatile, often Teflon or heparin –coated
Certain torque
Fixed or movable core

## Slide 4: Guide wires…
Different tip constructions
  Straight
  Angled
  J-shaped
Different length
Different diameters
  0.014 – 0.038’’
Different stiffness
Safety
Is it possible to bend the tip 180 degrees
Wrapped wire
  junction of stiff core to external coils/sleeve

## Slide 5
Guide wires for conventional use
Stiffness of guide wires of 0.035“
„Noodle“wire
Standard
Terumo wire
„Heavy duty“
Extra stiff
Super stiff
Ultra stiff
Back-up
Notes: 5
all wires except the noodle and terumo wire are more or less shapeable to individual needs

## Slide 6
Most catheters are not suitable
some coronary catheters …
Several MR-compatible
diagnostic catheters
are available
Notes: 6
MR-Catheter desireable

## Slide 7
The quality of imaging -
spatial resolution
extreme subatretic coarctation
Notes: 7
Extreme coarctation how to get through with MRI resolution?
Is there a communication or not?

## Slide 8
The quality of imaging
spatial resolution and stent-caused drop outs
Stiff guide wire is mandatory
Krueger, Circulation 2006
Notes: 8
Experience with the kind of stent artifact
Need for other stents???
Stability of balloon
Rapid pacing – making the procedure more complex
Stiff wire

## Slide 9
PMCF 11/2015 - 12/2016
Handling
Steerability
Visibility
Safety
Primary Endpoints
MR compatible guide wire
CE/FDA/Health Canada-certified guidewire
Diameter 0.035’’ (0.89 mm)
Length 180 cm
Notes: Secondary Endpoints
To confirm usability: Absence of MRWire related events such as damage to vessel walls, or other device related events
• To confirm feasibility: Absence of MRWire related events such as device deficiencies, obstruction in catheter, non-visibility in MRI (if guidewire related) and positive assessment of structural integrity
Prospective, multi-centre PMCF study with CE certified device.
Primary Endpoints 5.1.
Primary Endpoint: Procedural Success defined as “Was procedural success reached?”: yes/no
Procedural success (only during procedure) means that all of the following questions are answered with “yes”:
• Could the MRWire be inserted successfully through the introducer device (handling) ?
• Could the MRWire be introduced successfully to the anatomical target lesion (steerability) ?
• Was the MRWire sufficiently visible in MRI to allow steering to the target lesion (conspicuity) ?
And
the following question is answered with “no”:
Did any adverse event, related to the MRWire occur?
Secondary endpoints
• To confirm usability: Absence of MRWire related events such as damage to vessel walls, or other device related events
• To confirm feasibility: Absence of MRWire related events such as device deficiencies, obstruction in catheter, non-visibility in MRI (if guidewire related) and positive assessment of structural integrity

## Slide 10
Certification of guidewire 2.0 (teflon sleeve)
Europe December 2017
USA November 2017

## Slide 11: Clinical impression of our interventionalist
Overall impression:
good guide wire

## Slide 12: Conclusion
Guide wires with straight and angled tip available
Guide wires different stiffness still not available
Diagnostic cath is feasible in not too complex anatomies
Interventions for selected cases
Notes: 12
emergencies have to be anticipated.

## Slide 13
Safety issues and quality control
Select patients well
plan your emergency case
Notes: 13
emergencies have to be anticipated.

## Slide 14
Outlook
Need for interventionalists to get involved
Different wires for different purposes
Special catheters
Better imaging resolution